## Slide 1: DSL and Source to Source Compilation
João Bispo, Pedro Pinto, João Cardoso
Hands-on-approach and the Clava+LARA approach
2018-10-23 – PRACE School 2018

## Slide 2: Outline
Overview
  Clava
  LARA
Hands-on approach
  First LARA Strategy (Call Graph)
  Code Instrumentation (Logging)
  Clava APIs (Time and Energy Measurement)
  CMake Plugin (Auto-Parallelization)
  Third-party Libraries (DSE)

## Slide 3: Clava
Source-to-source C/C++ compiler (weaver)
User-defined strategies written in LARA
Several kinds of strategies possible
  Analysis, Generation, Insertion, Modification
Open-source
  github.com/specs-feup/clava
Notes: - Developed during the H2020 project ANTAREX
- During this tutorial we will show how to write several kinds of strategies

## Slide 4: Clava - Toolflow
LARAI
C/C++ Weaver
Client
JAVA
ClangDump.exe
CLAVA
(C/C++ AST)
ClangDump Parser
C++
Clang-based parser
Custom Clava AST
  AST-based transformations
LARA framework
Notes: Clang supports text-based transformations.
  Changing the AST does not reflect on the output code (does not support generating code from the AST)
Generic LARA interpreter, used as library
LARAI executes LARA code, Weaver Client answer requests from interpreter
  Maps code points specified in LARA (e.g., function, loop) to the corresponding nodes in the AST
When running a LARA strategy, we provide input source code, that will be parsed to an AST
This AST is implicit during the execution of the strategy

## Slide 5: The LARA Language
JavaScript-based language
Strategies written separately from application logic code
Not tied to a specific target language
  Weavers binds LARA code to a target language
  Current languages: Java, C, C++ and MATLAB
J. M.P. Cardoso, T. Carvalho, J. G. de F. Coutinho, W. Luk, R. Nobre, P. C. Diniz, Z. Petrov, “LARA: An Aspect-Oriented Programming Language for Embedded Systems,” in Int’l Conf. on Aspect-Oriented Software Development (AOSD’12), Potsdam, Germany, March 25-30, 2012.
aspectdef myAspect
end
input
in0, in1=3;
end
output
out0, out1;
end
function h() { }
var z = 2;
select … end apply … end condition … end
Notes:   - Weaving engine responsible to target a specific language

## Slide 6: Main LARA Features
Declarative select-apply clauses
  Select points of interest in the code
  Apply code transformations over them
Modularity and reuse based on calling aspects and using parameters
Composition of strategies based on other strategies
select method end
apply
…
end
apply
call LoopTiling(64);
call Timer("ns");
end

## Slide 7: LARA Select
Access points on the source code
Uses an hierarchical point chain
  Defined in the language specification
Points not present in the chain are inferred
Filtering based on attributes
select file.function.body.call end
select function.call end
select function{name==="draw"}.call end
Notes: Can combine different selects into a single chain
  Similar to an SQL “natural join”
  Useful when multiple join points are necessary to process during a join point iteration

## Slide 8: LARA Apply
Iterates over the selected points (prefixed with $)
Any point in the select statement can be accessed
Can access point attributes
Can change the application
select function{name=="draw"}.call end
apply
$call.insert before 'code to inject';
insert before 'more code';
end
$loop.exec interchange($innerLoop);
$var.def type='float';
insert before|after|replace
  For injecting code in input application source code
exec
  For executing a compiler action
def
  For defining the value of an attribute
Notes: - Apply can be seen as a for loop, that will iterate over the points obtained with the select

## Slide 9: LARA Reusability and Targetability
Reusable Strategies
Custom Targetability

## Slide 10: LARA Reusability and DSE
Reusable Between Different Languages
Design Exploration
Java
C
MATLAB
Java
C
MATLAB

## Slide 11: Hands-on
Getting Started
Objectives
  Open the Virtual Machine
  Find the tutorial folder
  Run Clava GUI

## Slide 12: Hands-on
1. CallGraph
Objectives
  Read some LARA code
  Load and run a LARA strategy

## Slide 13: Hands-on
2. Logging
Objectives
  Write some LARA code (exercise)
  Introduction to LARA APIs

## Slide 14: Hands-on
3. Measurements
Objectives
  Use LARA APIs (exercise)
  Introduction to Clava documentation

## Slide 15: Hands-on
4. AutoPar
Objectives
  Auto-parallelize code
  Introduction to CMake plugin

## Slide 16: Hands-on
5. Exploration
Objectives
  Use the CMake plugin
  Perform Design-Space Exploration

## Slide 17: Clava Installation
All platforms: download JAR
  http://specs.fe.up.pt/tools/clava.jar
Linux: script clava-update
  http://specs.fe.up.pt/tools/clava/clava-update
CMake Plugin:
  https://github.com/specs-feup/clava/tree/master/CMake

## Slide 18: Backup Slides

## Slide 19: The LARA Language
Join Point Model
  Allows the front-end to adapt to other target programming languages
Attribute Model
  Allows LARA to access join point values and to associate values to join points
Action Model
  Allows LARA to express actions
file
|\_var
|\_declaration
\_function
|\_prototype
\_body
|\_first
|\_last
|\_var
|\_call
|\_if
| |\_condition
| |\_then
| \_else
\_loop
|\_init
|\_condition
|\_counter
|\_body
\_control
attributes
|\_var
| |\_name
| |\_type
| |\_is_array
| |\_is_pointer
| |\_is_write
| |\_is_read
| |\_is_in
| \_is_out
|\_function
| |\_name
| |\_num_lines
| \_return_type
|\_call
| |\_name
| |\_return_type
| |\_num_argin
| \_num_argout
\_loop
|\_type
|\_is_innermost
|\_num_iterations
|\_increment_value
|\_rank
\_nested_level
Join Point Model
Attribute Model

## Slide 20: AOP Approach
Several AOP languages
No reusability between AOP languages
Flexibility on the join point capture
Include the support of code transformations
Existence of many crosscutting concerns!
Concerns related to code transformations and compiler optimizations:
  Performance, Power, Energy
  Parallelism, Concurrency
  Monitoring, Test, Debug
  Safety, Security
  Targeting hardware accelerators, multicore and manycore architectures
  Different tool flows
  Fully explore compiler optimizations
Notes: Several AOP languages
No reusability between AOP languages
  Important when dealing with different tool flows
Flexibility on the join point capture
  Easily add/remove new join point types
Include the support of code transformations beside code instrumentation and introduction
  type definitions
  compiler optimizations

## Slide 21: LARA Compilation Flow
WeaverGenerator
Notes: 21